## Slide 1: Webots Seminar
Wonse Jo
jow@purdue.edu
SMART LAB

## Slide 2: Contents
Introduction of Webots
Section 1: Create World and import Robot
  Create new world
  Import existing Robot platform
  Insert obstacles
  Control motor velocity
Section 2: Reading keyboard
  Read Keyboard
  Robot control
Brake time (5 min)
Section 3: Reading sensor
  Read and display distance sensor data
  Robot control with random walking
Section 4: Apply algorithm
  Read mouse position
  Apply position control algorithm

## Slide 3: Download Webots
Download Webots from https://cyberbotics.com/download
  Version R2019-revv1 : Window or Ubuntu

## Slide 4: Introduction of Webots
Webots?
  Open Source Robot Simulator
    provides a complete development environment to model, program and simulate robots.
    well documented and continuously maintained since 1996
  Thousands of institutions worldwide use it for R&D and teaching.
    used in industry, education and research
  Initially developed by Dr. Olivier Michel at the Swiss Federal Institute of Technology (EPFL) in Lausanne, Switzerland in 1996

## Slide 5: Introduction of Webots
Webots?
  Open Dynamics Engine (ODE)
    For detecting of collisions and simulating rigid body dynamics.
    Allows to accurately simulate physical properties of objects such as velocity, inertia, and friction.
  Robot controller programs written by C, C++, Python, ROS, Java, and MATLAB.
  There are a number of examples in the program or Website

## Slide 6: Introduction of Webots
Webots?
  Included 45 Robot Models: https://cyberbotics.com/doc/guide/robots

## Slide 7: Introduction of Webots
Webots?
  Included 45 Robot Models: https://cyberbotics.com/doc/guide/robots

## Slide 8: Introduction of Webots
Webots?
  Included 12 Acuator Models: https://cyberbotics.com/doc/guide/robots

## Slide 9: Introduction of Webots
Webots?
  Included 26 Sensor Models: https://cyberbotics.com/doc/guide/robots

## Slide 10: Introduction of Webots
Webots?
  Included 26 Sensor Models: https://cyberbotics.com/doc/guide/robots

## Slide 11: Introduction of Webots
Sphero's BB-8 robot model in Webots

## Slide 12: Introduction of Webots
Tinkerbots in Webots

## Slide 13: Introduction of Webots
Katana Robot Arm

## Slide 14: Introduction of Webots
KUKA's youBot

## Slide 15: Introduction of Webots
Real vs Simulation

## Slide 16: Import VRML File
Select VRML format
Click the option
Setup the output as
version = VRML 97,
Unit = Meter
Need to save as VRML files from 3D design Program
- Result

## Slide 17: Section 1
Create World and import Robot

## Slide 18: Section 1: Create World and import Robot
Run the Webots Program
Create New World for first simulation
  Click the Wizard
  Create “a Webots Project directory”
  Change a name for project
  Change a name for the new world

## Slide 19: Section 1: Create World and import Robot
3D Window
Scene Tree
Text editor
Console
Reload
Change Viewpoint
Play
Pause
Save
Add a new

## Slide 20: Section 1: Create World and import Robot

## Slide 21: Section 1: Create World and import Robot

## Slide 22: Section 1: Create World and import Robot
Import New robot and Obstacles
  Add “RectangleArena”
Add New -> PROTO nodes -> objects -> floors -> RectangleArena (Solid)
Or search “floor”

## Slide 23: Section 1: Create World and import Robot

## Slide 24: Section 1: Create World and import Robot
Modify the size of the floor
  enter “1” in x and y
Modify the height of the wall

## Slide 25: Section 1: Create World and import Robot
Modify the translation
  enter “0.5, 0, 0.5”

## Slide 26: Section 1: Create World and import Robot
Add e-Puck Robot
    PROTO nodes(Webots)/robots/gctronic/e-puck

## Slide 27: Section 1: Create World and import Robot
Setup DEF to make global variable
    Edit “e-puck” for controller code

## Slide 28: Section 1: Create World and import Robot
Add the cardboardBox in the world

## Slide 29: Section 1: Create World and import Robot
Modify the size of the box
X-axis
Z-axis
Y-axis

## Slide 30: Section 1: Create World and import Robot
Move the box
X-axis
Z-axis
Y-axis
(1) Drag the box with shift key
Or (2) Edit desire position

## Slide 31: Section 1: Create World and import Robot
Add mass “1”
  the box will drop into the floor

## Slide 32: Section 1: Create World and import Robot
Apply Force via mouse drag
  Click one of surface of the imported box
  Click the mouse left button with Alt key
  Then, drag

## Slide 33: Section 2
Basic robot control

## Slide 34: Section 2: Basic robot control
In section 2, we will
  Read keyboard data
  Control robot via keyboard

## Slide 35: Section 2: Basic robot control
Introduce e-Puck Robot
  Go to https://cyberbotics.com/doc/guide/robots
  Search “e-Puck”

## Slide 36: Section 2: Basic robot control
Procedures for controller programing
  Define Name:
    Ex) WbDeviceTag motor_wonsu
  Setup device property
    Ex) wb_motor_set_velocity()
  Read variables
    Ex) wb_motor_get_device()
int variable;
WbDeviceTag
Get data from node
A = function();
A = wb_motor_get_device()
Define Name
Set variables on node
void functions();
wb_motor_set_device();

## Slide 37: Section 2: Basic robot control
Create a New controller using Wizards
  Click the Wizard -> New Robot Controller -> Select C Language -> edit name
  Import this controller into e-Puck controller Node

## Slide 38: Section 2: Basic robot control
Control Motor velocity

## Slide 39: Section 2: Basic robot control
Refer “Nodes and API Functions”
  https://www.cyberbotics.com/doc/reference/nodes-and-api-functions
  Search “Motor”
  Go to Velocity control

## Slide 40: Section 2: Basic robot control
Control Motor velocity (Left Motor)
  #include <stdio.h>
  #include <stdlib.h>
  #include <webots/robot.h>
  #include <webots/motor.h>
  #define TIME_STEP 64
  #define MAX_SPEED 6.28
  int main(int argc, char **argv)
  {
  /* necessary to initialize webots stuff */
  wb_robot_init();
  // get the motor devices
  WbDeviceTag left_motor = wb_robot_get_device("left wheel motor");
  // set the target position of the motors
  wb_motor_set_position(left_motor, INFINITY);
  wb_motor_set_velocity(left_motor, 0);
  /* main loop
  * Perform simulation steps of TIME_STEP milliseconds
  * and leave the loop when the simulation is over
  */
  while (wb_robot_step(TIME_STEP) != -1) {
  wb_motor_set_velocity(left_motor, MAX_SPEED);
  };
  /* Enter your cleanup code here */
  /* This is necessary to cleanup webots resources */
  wb_robot_cleanup();
  return 0;
  }

## Slide 41: Section 2: Basic robot control
Control Motor velocity
  Before compiling controller, recommend to save the world

## Slide 42: Section 2: Basic robot control
Control Motor velocity
    (Q1) Add “MAX_SPEED” to the right motor

## Slide 43: Section 2: Basic robot control
Control Motor velocity
  #include <stdio.h>
  #include <stdlib.h>
  #include <webots/robot.h>
  #include <webots/motor.h>
  #define TIME_STEP 64
  #define MAX_SPEED 6.28
  int main(int argc, char **argv)
  {
  /* necessary to initialize webots stuff */
  wb_robot_init();
  // get the motor devices
  WbDeviceTag left_motor = wb_robot_get_device("left wheel motor");
  WbDeviceTag right_motor = wb_robot_get_device("right wheel motor");
  // set the target position of the motors
  wb_motor_set_position(left_motor, INFINITY);
  wb_motor_set_position(right_motor, INFINITY);
  wb_motor_set_velocity(left_motor, 0);
  wb_motor_set_velocity(right_motor, 0);
  /* main loop
  * Perform simulation steps of TIME_STEP milliseconds
  * and leave the loop when the simulation is over
  */
  while (wb_robot_step(TIME_STEP) != -1) {
  wb_motor_set_velocity(left_motor, MAX_SPEED);
  wb_motor_set_velocity(right_motor, MAX_SPEED);
  };
  /* Enter your cleanup code here */
  /* This is necessary to cleanup webots resources */
  wb_robot_cleanup();
  return 0;
  }

## Slide 44: Section 2: Basic robot control
Enable keyboard input
  Add a keyboard function (refer API website)
    https://www.cyberbotics.com/doc/reference/keyboard

## Slide 45: Section 2: Basic robot control
Enable keyboard input
  Add: #include <webots/keyboard.h>
  In main ():
    Add: wb_keyboard_enable(TIME_STEP);
  In while loop
    Add: printf("%d \n", wb_keyboard_get_key());
  Run the code

## Slide 46: Section 2: Basic robot control
(Q2) Control the e-puck using keyboard
  Hint
    Find returned values on console when clicking the keyboard
      -1 = none
    Use if-else loop
    Give different velocity based on the type of the key.

## Slide 47: Section 2: Basic robot control
#include <stdio.h>
#include <stdlib.h>
#include <webots/robot.h>
#include <webots/motor.h>
#include <webots/keyboard.h>
#define TIME_STEP 64
#define MAX_SPEED 6.28
int main(int argc, char **argv)
{
wb_robot_init();
WbDeviceTag left_motor = wb_robot_get_device("left wheel motor");
WbDeviceTag right_motor = wb_robot_get_device("right wheel motor");
wb_motor_set_position(left_motor, INFINITY);
wb_motor_set_position(right_motor, INFINITY);
wb_motor_set_velocity(left_motor, 0);
wb_motor_set_velocity(right_motor, 0);
wb_keyboard_enable(TIME_STEP);
int key_value = 0;
while (wb_robot_step(TIME_STEP) != -1) {
key_value = wb_keyboard_get_key();
if (key_value == 315){
wb_motor_set_velocity(left_motor, 0.3*MAX_SPEED);
wb_motor_set_velocity(right_motor, 0.3*MAX_SPEED);
}
else if(key_value == 317){
wb_motor_set_velocity(left_motor, -0.3*MAX_SPEED);
wb_motor_set_velocity(right_motor, -0.3*MAX_SPEED);
}
else if(key_value == 314){
wb_motor_set_velocity(left_motor, -0.3*MAX_SPEED);
wb_motor_set_velocity(right_motor, 0.3*MAX_SPEED);
}
else if(key_value == 316){
wb_motor_set_velocity(left_motor, 0.3*MAX_SPEED);
wb_motor_set_velocity(right_motor, -0.3*MAX_SPEED);
}
else{
wb_motor_set_velocity(left_motor, 0);
wb_motor_set_velocity(right_motor, 0);
}
};
wb_robot_cleanup();
return 0;
}

## Slide 48: Brake Time
5 min

## Slide 49: Section 3
Reading sensor data

## Slide 50: Section 3: Reading sensor data
In section 3, we will
  Read distance sensor data
  Display data on the world
  Apply collision avoidances

## Slide 51: Section 3: Reading sensor data
E-puck 2
  There are 8 distance sensors.
    Name: ps0, ps1, ps2, ps3, ps4, ps5, ps6, ps7.

## Slide 52: Section 3: Reading sensor data
Controller Code
  Add distance_sensor.h
    #include <webots/distance_sensor.h>
  Define distance sensor name
    WbDeviceTag wonsu_ps0 =wb_robot_get_device(“ps0”)
  Enable distance sensor
    wb_distance_sensor_enable(wonsu_ps0, TIME_STEP);
  Get sensor data from the sensor
    double ps_0_value = 0;
    ps_0_value = wb_distance_sensor_get_value(wonsu_ps0);
  Display the data
    printf(“%f \n”, ps_0_value);

## Slide 53: Section 3: Reading sensor data
(Q3) Enable a distance sensor and display both ps1 and p7
  Hint: Add new enable sensor function and change of sensor name (p7)

## Slide 54: Section 3: Reading sensor data
Controller Code
  In mian ()
    WbDeviceTag wonsu_ps0 = wb_robot_get_device("ps0");
    WbDeviceTag wonsu_ps7 = wb_robot_get_device("ps7");
    wb_distance_sensor_enable(wonsu_ps0, TIME_STEP);
    wb_distance_sensor_enable(wonsu_ps7, TIME_STEP);
  In while loop
    ps0_data = wb_distance_sensor_get_value(wonsu_ps0);
    ps7_data = wb_distance_sensor_get_value(wonsu_ps7);
    printf("ps0 = %f, ps7 = %f \n", ps0_data, ps7_data);

## Slide 55: Section 3: Reading sensor data
(Q4) Add random walking to e-puck with collision avoidance
  Don’t remove keyboard function
  Add rand() function to make random velocity
  If ps data exceeds 60, change the velocity of left and right motor

## Slide 56: Section 3: Reading sensor data
Add random walking to e-puck with collision avoidance
  if(key_value != -1) { ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~}
  else
  {
  if (ps7_data > 100) {
  // turn right
  left_speed += 0.5 * MAX_SPEED;
  right_speed -= 0.5 * MAX_SPEED;
  }
  else if (ps0_data > 70) {
  // turn left
  left_speed -= 0.5 * MAX_SPEED;
  right_speed += 0.5 * MAX_SPEED;
  }
  else if( ps7_data > 70 || ps0_data > 70){
  left_speed = -MAX_SPEED;
  right_speed = -MAX_SPEED;
  }
  else
  {
  left_speed = (int)rand()%((int)MAX_SPEED + 1 - 0) + 0;
  right_speed = (int)rand()%((int)MAX_SPEED + 1 - 0) + 0;
  }
  if (left_speed > MAX_SPEED){
  left_speed = MAX_SPEED;
  }
  if (left_speed < -MAX_SPEED){
  left_speed = -MAX_SPEED;
  }
  if (right_speed > MAX_SPEED){
  right_speed = MAX_SPEED;
  }
  if (right_speed < -MAX_SPEED){
  right_speed = -MAX_SPEED;
  }
  wb_motor_set_velocity(left_motor, left_speed);
  wb_motor_set_velocity(right_motor, right_speed);
  }

## Slide 57: Section 4
Apply algorithm

## Slide 58: Section 4: Apply algorithm
Apply Go-to-Goal Algorithm on Webots

## Slide 59: Section 4: Apply algorithm
Add Supervisor Node to get a current position and heading angle of the e-puck
  Add webots/supervisor.h
    #include <webots/supervisor.h>
  Define NodeRef, and WbfieldRef to get the robot’s position and heading angle
    WbNodeRef mybot = wb_supervisor_node_get_from_def("e-puck"); // DEF name
    WbFieldRef rotationFieldWbFieldRef translationField = wb_supervisor_node_get_field(mybot, "translation");
    WbFieldRef rotationField = wb_supervisor_node_get_field(mybot, "rotation");
  Get current position and heading angle from e-puck Node
    const double *translation = wb_supervisor_field_get_sf_vec3f(translationField);
    const double *rotation = wb_supervisor_field_get_sf_rotation(rotationField);
  Display the data
    printf("%f, %f, %f \n", translation[0], translation[2], rotation[3]);

## Slide 60: Section 4: Apply algorithm
Please visit the link to copy and paste the code
  https://github.com/wonsu0513/webot_seminar/blob/master/mouse_key_motor.txt

## Slide 61: Section 4: Apply algorithm
(Q5) Apply position control algorithm used in the assignment.
  If you click a position on the floor, robot should go to the position using the position control algorithm.
    Hint:
      Add 5 CardboardBox and spread randomly them on the floor
      Apply obstacle avoidance
      Add Mouse Node to select goal position
      Apply go-to-goal algorithm used in the HW
        Make a new function to return two variables (vR, vL)
          double* robot_controller(double* start_pos, double* target_pos) {
            // your code
            return motor_velocity;
          }
        Change the matlab code into C Language.
        Move robot to Initial point (0.1, 0, 0.01)
        If click some position, robot should go to the point.

## Slide 62: Section 4: Apply algorithm

## Slide 63: Thanks